## Slide 1
Vitis HLS + PMOD
C/C++에서 RTL 생성 및 커스텀 IP 개발
KV260 FPGA Training Series

## Slide 2
학습 목표
2
Step 04: Vitis HLS + PMOD — C/C++에서 RTL 생성 및 커스텀 IP개발
Vitis HLS 이해
C/C++에서 RTL 생성
PMOD IP 개발
PetaLinux 연동
난이도: ★★★☆☆ (중급) | 소요 시간: 약 3~4시간

## Slide 3
Vitis HLS 이해
2
Step 04: Vitis HLS + PMOD — C/C++에서 RTL 생성 및 커스텀 IP개발
High-Level Synthesis
C/C++  Verilog/VHDL
성능 최적화
Vitis HLS에서 C++ 코드작성
C Synthesis 실행
Export RTL
(IP Catalog 형식)
Vivado에서 커스텀 IP추가
Bitstream 생성
( 전체 흐름)

## Slide 4
Vitis HLS
2
Step 04: Vitis HLS + PMOD — C/C++에서 RTL 생성 및 커스텀 IP개발
Step 1: 프로젝트 생성
  1.1 Vivado 실행
    source /tools/Xilinx/Vivado/2021.2/settings64.sh
    Vitis_hls &
  Project Name: pmod_io_ip
  Top Function: pmod_io
  Part: xck26-sfvc784-2LV-c (KV260)

## Slide 5
code
Vitis HLS
2
Step 04: Vitis HLS + PMOD — C/C++에서 RTL 생성 및 커스텀 IP개발
Step 2: C++ 코드 작성
    #include <stdio.h>
    #include <stdint.h>
    Typedef unsigned short int u16;
    U16 pmod_io(u16 io_ctrl, u16 io_num, u16& pmod) {
      #pragma HLS INTERFACE ap_ctrl_none port=return
      #pragma HLS INTERFACE s_axilite port=io_ctrl
      #pragma HLS INTERFACE s_axilite port=io_num
      #pragma HLS INTERFACE s_axilite port=pmod
      static u16 pmod_mask = 0;
      If (io_ctrl == 0xf) {
        pmod_mask = 0; //초기화
      } else if (io_ctrl == 0xa) {
        pmod_mask = (1 << io_num); // SET
      } else if (io_ctrl == 0x5) {
        pmod_mask = ~(1 << io_num); // CLEAR
  } else if (io_ctrl == 0x1) {
        pmod_mask = io_num; // WRITE
      }
      pmod = pmod_mask;
      return pmod_mask;
    }

## Slide 6
Vitis HLS
2
Step 04: Vitis HLS + PMOD — C/C++에서 RTL 생성 및 커스텀 IP개발
  2.1 C++코드 동작 설명
Io_ctrl | 동작
0xf | 초기화
0xa | 비트 SET
0x5 | 비트 CLEAR
0x1 | 직접 쓰기
0x0 | 읽기
Step 3: C Synthesis
  Run C Syntheis 버튼 클릭 후 리포트 확인

## Slide 7
Vitis HLS
2
Step 04: Vitis HLS + PMOD — C/C++에서 RTL 생성 및 커스텀 IP개발
Step 4: RTL Export
  Export RTL 클릭
  Format: IP Catalog
  export.zip 생성 확인
Step 5: Vivado에서 프로젝트 생성
  source /tools/Xilinx/Vivado/2021.2/settings64.sh
  vivado &
  Create Project: RTL Project
  Name: kv260_pmod_demo
  Board: Kria KV260 Vision AI Starter Kit

## Slide 8
Vitis HLS
Step 6: IP Repository 추가
  Setting  IP  Repository
  Pmod_io_ip/export.zip 추가
2
Step 04: Vitis HLS + PMOD — C/C++에서 RTL 생성 및 커스텀 IP개발
Step 7: Block Diagram 구성
  pmod_io IP 추가
  axi_gpio 추가 (GPIO Width: 4)
  slice IP 추가 (16bit  8bit)
  Run Connection Automation

## Slide 9
Vitis HLS
Step 8: Pin Constraints (XDC)
2
Step 04: Vitis HLS + PMOD — C/C++에서 RTL 생성 및 커스텀 IP개발
Step 9: Block Diagram 구성
  pmod_io IP 추가
  axi_gpio 추가 (GPIO Width: 4)
  slice IP 추가 (16bit  8bit)
  Run Connection Automation
# PMOD J1
set_property PACKAGE_PIN H12 [get_ports pmod[0]]
set_property PACKAGE_PIN E10 [get_ports pmod[1]]
set_property PACKAGE_PIN D10 [get_ports pmod[2]]
set_property PACKAGE_PIN C11 [get_ports pmod[3]]
set_property IOSTANDARD LVCMOS33 [get_ports pmod[*]]
set_property SLEW SLOW [get_ports pmod[*]]
set_property DRIVE 4 [get_ports pmod[*]]

## Slide 10
Vitis HLS
Step 8: Pin Constraints (XDC)
2
Step 04: Vitis HLS + PMOD — C/C++에서 RTL 생성 및 커스텀 IP개발
Reference to .md file